## Slide 1: LEGO MINDSTORMS EV3Dev and Raspberry Pi Communicator

## Slide 2: Objectives
Learn how to make send commands from an EV3 to a Raspberry Pi using ev3dev
Prerequisites:
  Must be comfortable using a Raspberry Pi (Unix/Linux commands) and some basic Python
  Must be familiar with ev3dev
  Complete the EV3Lessons Introduction of ev3dev Lesson

## Slide 3: Materials
Raspberry Pi (Tested on Model B Edition 1 using Raspbian)
EV3 brick
USB WIFI for EV3 (or another way of connecting to the internet)
Ethernet/WIFI for Raspberry Pi
Micro SD card with ev3dev on it (Insert into EV3’s microSD slot)

## Slide 4: Step 1: Setup
You will need to be a root/admin user on both devices
Install software on the Raspberry Pi
  sudo raspi-config
  Enable SSH  Yes
Install software on the EV3 (you will need to ssh the EV3) The paramiko software will allow you to use ssh from inside python on the EV3.
  sudo apt-get install python-pip
  sudo pip install paramiko

## Slide 5: Step 3: Base Code
The code below is run on the EV3
  This will send a command to the Raspberry Pi
  This assumes that you Pi’s full hostname is raspberrypi.home
  This assumes that your username is pi and password raspberry
Replace COMMAND_HERE below with the command you want to execute on the Pi
import paramiko #import software
client = paramiko.SSHClient() #start ssh client.set_missing_host_key_policy(paramiko.AutoAddPolicy()) #do not give warnings client.connect('raspberrypi.home', username='pi', password='raspberry') #connect to pi stdin, stdout, stderr = client.exec_command(‘COMMAND_HERE') #send a command for line in stdout: #collect command output lines print line.strip('\n') #print output
client.close() #disconnect from pi
CHALLENGE: write a program to list files on the Pi using the EV3

## Slide 6: Challenge: Solution
import paramiko #import software
#start ssh
client = paramiko.SSHClient()
#do not give warnings
client.set_missing_host_key_policy(paramiko.AutoAddPolicy())
#connect to pi
client.connect('raspberrypi.home', username='pi', password='raspberry')
#send a command
stdin, stdout, stderr = client.exec_command(‘ls’)
for line in stdout: #collect command output lines
print line.strip('\n') #print output
client.close() #disconnect from pi

## Slide 7: CREDITS
This tutorial was created by Sanjay Seshan and Arvind Seshan from Droids Robotics.
More lessons are available at www.ev3lessons.com
Author’s Email: team@droidsrobotics.org
Credits: ev3dev.org
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.